## Slide 1: Introduction to CUDA C
Slide credit: Slides adapted from
© David Kirk/NVIDIA and Wen-mei W. Hwu, 2007-2016

## Slide 2: CPU and GPU are designed very differently
CPU
Latency Oriented Cores
Chip
Core
Local Cache
Registers
SIMD Unit
Control
GPU
Throughput Oriented Cores
Chip
Compute Unit
Cache/Local Mem
Registers
SIMD Unit
Threading

## Slide 3: CPUs: Latency Oriented Design
Powerful ALU
  Reduced operation latency
Large caches
  Convert long latency memory accesses to short latency cache accesses
Sophisticated control
  Branch prediction for reduced branch latency
  Data forwarding for reduced data latency
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU

## Slide 4: GPUs: Throughput Oriented Design
Small caches
  To boost memory throughput
Simple control
  No branch prediction
  No data forwarding
Energy efficient ALUs
  Many, long latency but heavily pipelined for high throughput
Require massive number of threads to tolerate latencies
  Threading logic
  Thread state
DRAM
GPU

## Slide 5: Applications Use Both CPU and GPU
CPUs for sequential parts where latency matters
  CPUs can be 10X+ faster than GPUs for sequential code
GPUs for parallel parts where throughput wins
  GPUs can be 10X+ faster than CPUs for parallel code

## Slide 6: Objective
To learn the main venues and developer resources for GPU computing
  Where CUDA C fits in the big picture

## Slide 7: 3 Ways to Accelerate Applications
Applications
Libraries
Easy to use
Most Performance
Programming Languages
Most Performance
Most Flexibility
Easy to use
Portable code
Compiler Directives

## Slide 8: Libraries: Easy, High-Quality Acceleration
Ease of use: Using libraries enables GPU acceleration without in-depth knowledge of GPU programming
“Drop-in”: Many GPU-accelerated libraries follow standard APIs, thus enabling acceleration with minimal code changes
Quality: Libraries offer high-quality implementations of functions encountered in a broad range of applications
Notes: Developing applications around libraries offers a range of benefits:
- Being callable from your host application, the CUDA accelerated libraries can hide a lot of the architectural details of the GPUs and therefore significantly shorten your application development
cycle.
CUDA-accelerated libraries often use APIs similar to well established libraries widely used
in scientific applications, thus enabling a drop-in acceleration experience. In some cases, the
libraries will offer exactly the same interface for both the GPU accelerated Version and the CPU
only version, resulting in code portable between the worlds. In other cases, some with a minimal
amount of code changes will be necessary to accommodate both CPU and GPU support.
Designing an application around libraries is also good software engineering practice, as it
reuses well tested code and therefore enhancing the overall quality of your application.
- Finally, CUDA accelerated libraries developed by NVIDIA engineers are highly tuned for
Performance, delivering excellent performance on every generation of GPUs, while maintaining generality.

## Slide 9: GPU Accelerated Libraries
Linear Algebra
FFT, BLAS,
SPARSE, Matrix
Numerical & Math
RAND, Statistics
Data Struct. & AI
Sort, Scan, Zero Sum
Visual Processing
Image & Video
NVIDIA
cuFFT,
cuBLAS,
cuSPARSE
NVIDIA
Math Lib
NVIDIA cuRAND
NVIDIA
NPP
NVIDIA
Video Encode
GPU AI – Board Games
GPU AI – Path Finding
Notes: GPU Accelerated libraries provide “drop-in” acceleration for your applications.
There are a wide variety of computational libraries available. You are probably familiar with the FFTW fast fourier transform library, the various BLAS linear algebra libraries,
the Intel Math Kernel Library, or Intel Performance Primitives library, to name a few. There are compatible GPU-accelerated libraries available as drop-in replacements
for all of the libraries I just mentioned, and many more.
cuBLAS is NVIDIA’s GPU-accelerated BLAS linear algebra library, which includes very fast dense matrix and vector computations.
cuFFT is NVIDIA’s GPU-accelerated Fast Fourier Transform Library.
cuRAND is NVIDIA’s GPU-accelerated random number generation library, which is useful in Monte Carlo algorithms and financial applications, among others.
cuSPARSE is NVIDIA’s Sparse matrix library, which includes sparse matrix-vector multiplication, fast sparse linear equation solvers, and tridiagonal solvers.
NVIDIA Performance Primitives includes literally thousands of signal and image processing functions.
Thrust is an open-source C++ Template library of parallel algorithms such as sorting, reductions, searching, and set operations.
And there are many more libraries available from third-party developers and open source projects.
GPU-accelerated libraries are the most straightforward way to add GPU acceleration to applications, and in many cases their performance cannot be beat.

## Slide 10: Compiler Directives: Easy, Portable Acceleration
Ease of use: Compiler takes care of details of parallelism management and data movement
Portable: The code is generic, not specific to any type of hardware and can be deployed into multiple languages
Uncertain: Performance of code can vary across compiler versions
Notes: Developing applications around libraries offers a range of benefits:
- Being callable from your host application, the CUDA accelerated libraries can hide a lot of the architectural details of the GPUs and therefore significantly shorten your application development
cycle.
CUDA-accelerated libraries often use APIs similar to well established libraries widely used
in scientific applications, thus enabling a drop-in acceleration experience. In some cases, the
libraries will offer exactly the same interface for both the GPU accelerated Version and the CPU
only version, resulting in code portable between the worlds. In other cases, some with a minimal
amount of code changes will be necessary to accommodate both CPU and GPU support.
Designing an application around libraries is also good software engineering practice, as it
reuses well tested code and therefore enhancing the overall quality of your application.
- Finally, CUDA accelerated libraries developed by NVIDIA engineers are highly tuned for
Performance, delivering excellent performance on every generation of GPUs, while maintaining generality.

## Slide 11: OpenACC
Compiler directives for C, C++, and FORTRAN
#pragma acc parallel loop copyin(input1[0:inputLength],input2[0:inputLength]), copyout(output[0:inputLength])
for(i = 0; i < inputLength; ++i) {
output[i] = input1[i] + input2[i];
}

## Slide 12: Programming Languages: Most Performance and Flexible Acceleration
Performance: Programmer has best control of parallelism and data movement
Flexible: The computation does not need to fit into a limited set of library patterns or directive types
Verbose: The programmer often needs to express more details

## Slide 13: GPU Programming Languages
CUDA Fortran
Fortran
CUDA C
C
CUDA C++
C++
PyCUDA, Copperhead, Numba
Python
Alea.cuBase
F#
MATLAB, Mathematica, LabVIEW
Numerical analytics
Notes: In this presentation I will talk about a variety of available GPU programming languages and interfaces. The languages include C, C++, C#, Fortran, Python, and numerical analytics packages such as MATLAB, Mathematica, and LabVIEW.

## Slide 14: CUDA - C
Applications
Libraries
Easy to use
Most Performance
Programming Languages
Most Performance
Most Flexibility
Easy to use
Portable code
Compiler Directives

## Slide 15: Memory Allocation and Data Movement API Functions

## Slide 16: Objective
To learn the basic API functions in CUDA host code
  Device Memory Allocation
  Host-Device Data Transfer

## Slide 17: Data Parallelism - Vector Addition Example
A[0]
vector A
vector B
vector C
A[1]
A[2]
A[N-1]
B[0]
B[1]
B[2]
…
…
B[N-1]
C[0]
C[1]
C[2]
C[N-1]
…
+
+
+
+

## Slide 18: Vector Addition – Traditional C Code
// Compute vector sum C = A + B
void vecAdd(float *h_A, float *h_B, float *h_C, int n)
{
int i;
for (i = 0; i<n; i++) h_C[i] = h_A[i] + h_B[i];
}
int main()
{
// Memory allocation for h_A, h_B, and h_C
// I/O to read h_A and h_B, N elements
…
vecAdd(h_A, h_B, h_C, N);
}

## Slide 19: Heterogeneous Computing vecAdd CUDA Host Code
CPU
Host Memory
GPU
Device Memory
Part 1
Part 3
#include <cuda.h>
void vecAdd(float *h_A, float *h_B, float *h_C, int n)‏
{
int size = n* sizeof(float);
float *d_A, *d_B, *d_C;
// Part 1
// Allocate device memory for A, B, and C
// copy A and B to device memory
// Part 2
// Kernel launch code – the device performs the actual vector addition
// Part 3
// copy C from the device memory
// Free device vectors
}
Part 2

## Slide 20: Partial Overview of CUDA Memories
Device code can:
  R/W per-thread registers
  R/W all-shared global memory
Host code can
  Transfer data to/from per grid global memory
We will cover more memory types and more sophisticated memory models later.
Host
(Device) Grid
Global
Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 21: CUDA Device Memory Management API functions
cudaMalloc()
  Allocates an object in the device global memory
  Two parameters
    Address of a pointer to the allocated object
    Size of allocated object in terms of bytes
cudaFree()
  Frees object from device global memory
  One parameter
    Pointer to freed object
Host
(Device) Grid
Global
Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers

## Slide 22: Host-Device Data Transfer API functions
cudaMemcpy()
  memory data transfer
  Requires four parameters
    Pointer to destination
    Pointer to source
    Number of bytes copied
    Type/Direction of transfer
  Transfer to device is asynchronous
Host
(Device) Grid
Global
Memory
Block (0, 0)
Thread (0, 0)
Registers
Block (0, 1)
Thread (0, 0)
Registers
Thread (0, 1)
Registers
Thread (0, 1)
Registers

## Slide 23: Vector Addition Host Code
void vecAdd(float *h_A, float *h_B, float *h_C, int n)
{
int size = n * sizeof(float); float *d_A, *d_B, *d_C;
cudaMalloc((void **) &d_A, size);
cudaMemcpy(d_A, h_A, size, cudaMemcpyHostToDevice);
cudaMalloc((void **) &d_B, size);
cudaMemcpy(d_B, h_B, size, cudaMemcpyHostToDevice);
cudaMalloc((void **) &d_C, size);
// Kernel invocation code – to be shown later
cudaMemcpy(h_C, d_C, size, cudaMemcpyDeviceToHost);
cudaFree(d_A); cudaFree(d_B); cudaFree (d_C);
}

## Slide 24: In Practice, Check for API Errors in Host Code
cudaError_t err = cudaMalloc((void **) &d_A, size);
if (err != cudaSuccess) {
printf(“%s in %s at line %d\n”, cudaGetErrorString(err), __FILE__,
__LINE__);
exit(EXIT_FAILURE);
}
10

## Slide 25: Threads and Kernel Functions

## Slide 26: Objective
To learn about CUDA threads, the main mechanism for exploiting of data parallelism
  Hierarchical thread organization
  Launching parallel execution
  Thread index to data index mapping
2

## Slide 27: Data Parallelism - Vector Addition Example
A[0]
vector A
vector B
vector C
A[1]
A[2]
A[N-1]
B[0]
B[1]
B[2]
…
…
B[N-1]
C[0]
C[1]
C[2]
C[N-1]
…
+
+
+
+

## Slide 28: CUDA Execution Model
Heterogeneous host (CPU) + device (GPU) application C program
  Serial parts in host C code
  Parallel parts in device SPMD kernel code
Serial Code (host)‏
. . .
. . .
Parallel Kernel (device)‏
KernelA<<< nBlk, nTid >>>(args);
Serial Code (host)‏
Parallel Kernel (device)‏
KernelB<<< nBlk, nTid >>>(args);

## Slide 29: A Thread as a Von-Neumann Processor
A thread is a “virtualized” or “abstracted”
Von-Neumann Processor
Memory
Control Unit
I/O
ALU
Reg
File
PC
IR
Processing Unit
Notes: Insert von-neumann schematic here

## Slide 30: Arrays of Parallel Threads
A CUDA kernel is executed by a grid (array) of threads
  All threads in a grid run the same kernel code (Single Program Multiple Data)‏
  Each thread has indexes that it uses to compute memory addresses and make control decisions
…
0
1
2
254
255
…
C[i] = A[i] + B[i];
i = blockIdx.x * blockDim.x + threadIdx.x;

## Slide 31: Thread Blocks: Scalable Cooperation
Divide thread array into multiple blocks
  Threads within a block cooperate via shared memory, atomic operations and barrier synchronization
  Threads in different blocks do not interact
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
0
1
2
254
255
Thread Block 0
…
1
2
254
255
Thread Block 1
0
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
1
2
254
255
Thread Block N-1
0
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
…
…
…

## Slide 32: blockIdx and threadIdx
Each thread uses indices to decide what data to work on
  blockIdx: 1D, 2D, or 3D (CUDA 4.0)
  threadIdx: 1D, 2D, or 3D
Simplifies memory addressing when processing multidimensional data
  Image processing
  Solving PDEs on volumes
  …
device
Grid
Block (0, 0)
Block (1, 1)
Block (1, 0)
Block (0, 1)
Block (1,1)
Thread
(0,0,0)
Thread
(0,1,3)
Thread
(0,1,0)
Thread
(0,1,1)
Thread
(0,1,2)
Thread
(0,0,0)
Thread
(0,0,1)
Thread
(0,0,2)
Thread
(0,0,3)
(1,0,0)
(1,0,1)
(1,0,2)
(1,0,3)