## Slide 1: Parallel Computation Patterns (Histogram)
Slide credit: Slides adapted from
© David Kirk/NVIDIA and Wen-mei W. Hwu, 2007-2016

## Slide 2: Histogram
A method for extracting notable features and patterns from large data sets
  Feature extraction for object recognition in images
  Fraud detection in credit card transactions
  Correlating heavenly object movements in astrophysics
  …
Basic histograms - for each element in the data set, use the value to identify a “bin counter” to increment

## Slide 3: A Text Histogram Example
Define the bins as four-letter sections of the alphabet: a-d, e-h, i-l, n-p, …
For each character in an input string, increment the appropriate bin counter.
In the phrase “Programming Massively Parallel Processors” the output histogram is shown below:

## Slide 4: A simple parallel histogram algorithm
Partition the input into sections
Have each thread to take a section of the input
Each thread iterates through its section.
For each letter, increment the appropriate bin counter

## Slide 5: Sectioned Partitioning (Iteration #1)

## Slide 6: Sectioned Partitioning (Iteration #2)

## Slide 7: Input Partitioning Affects Memory Access Efficiency
Sectioned partitioning results in poor memory access efficiency
  Adjacent threads do not access adjacent memory locations
  Accesses are not coalesced
  DRAM bandwidth is poorly utilized

## Slide 8: Input Partitioning Affects Memory Access Efficiency
Sectioned partitioning results in poor memory access efficiency
  Adjacent threads do not access adjacent memory locations
  Accesses are not coalesced
  DRAM bandwidth is poorly utilized
Change to interleaved partitioning
  All threads process a contiguous section of elements
  They all move to the next section and repeat
  The memory accesses are coalesced
1
1
1
1
1
2
2
2
2
2
3
3
3
3
3
4
4
4
4
4
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4

## Slide 9: Interleaved Partitioning of Input
For coalescing and better memory access performance
…

## Slide 10: Interleaved Partitioning (Iteration 2)
…

## Slide 11: Data races

## Slide 12: Objective
To understand data races in parallel computing
  Data races can occur when performing read-modify-write operations
  Data races can cause errors that are hard to reproduce
  Atomic operations are designed to eliminate such data races

## Slide 13: Read-modify-write in the Text Histogram Example
For coalescing and better memory access performance
…

## Slide 14: Read-Modify-Write Used in Collaboration Patterns
For example, multiple bank tellers count the total amount of cash in the safe
Each grab a pile and count
Have a central display of the running total
Whenever someone finishes counting a pile, read the current running total (read) and add the subtotal of the pile to the running total (modify-write)
A bad outcome
  Some of the piles were not accounted for in the final total

## Slide 15: A Common Parallel Service Pattern
For example, multiple customer service agents serving waiting customers
The system maintains two numbers,
  the number to be given to the next incoming customer (I)
  the number for the customer to be served next (S)
The system gives each incoming customer a number (read I) and increments the number to be given to the next customer by 1 (modify-write I)
A central display shows the number for the customer to be served next
When an agent becomes available, he/she calls the number (read S) and increments the display number by 1 (modify-write S)
Bad outcomes
  Multiple customers receive the same number, only one of them receives service
  Multiple agents serve the same number

## Slide 16: A Common Arbitration Pattern
For example, multiple customers booking airline tickets in parallel
Each
  Brings up a flight seat map (read)
  Decides on a seat
  Updates the seat map and marks the selected seat as taken (modify-write)
A bad outcome
  Multiple passengers ended up booking the same seat

## Slide 17: Data Race in Parallel Thread Execution
Old and New are per-thread register variables.
Question 1: If Mem[x] was initially 0, what would the value of Mem[x] be after threads 1 and 2 have completed?
Question 2: What does each thread get in their Old variable?
Unfortunately, the answers may vary according to the relative execution timing between the two threads, which is referred to as a data race.
thread1:
thread2:
Old  Mem[x]
New  Old + 1
Mem[x]  New
Old  Mem[x]
New  Old + 1
Mem[x]  New

## Slide 18: Timing Scenario #1
Time | Thread 1 | Thread 2
1 | (0) Old  Mem[x] | 
2 | (1) New  Old + 1 | 
3 | (1) Mem[x]  New | 
4 |  | (1) Old  Mem[x]
5 |  | (2) New  Old + 1
6 |  | (2) Mem[x]  New
Thread 1 Old = 0
Thread 2 Old = 1
Mem[x] = 2 after the sequence

## Slide 19: Timing Scenario #2
Time | Thread 1 | Thread 2
1 |  | (0) Old  Mem[x]
2 |  | (1) New  Old + 1
3 |  | (1) Mem[x]  New
4 | (1) Old  Mem[x] | 
5 | (2) New  Old + 1 | 
6 | (2) Mem[x]  New | 
Thread 1 Old = 1
Thread 2 Old = 0
Mem[x] = 2 after the sequence

## Slide 20: Timing Scenario #3
Time | Thread 1 | Thread 2
1 | (0) Old  Mem[x] | 
2 | (1) New  Old + 1 | 
3 |  | (0) Old  Mem[x]
4 | (1) Mem[x]  New | 
5 |  | (1) New  Old + 1
6 |  | (1) Mem[x]  New
Thread 1 Old = 0
Thread 2 Old = 0
Mem[x] = 1 after the sequence

## Slide 21: Timing Scenario #4
Time | Thread 1 | Thread 2
1 |  | (0) Old  Mem[x]
2 |  | (1) New  Old + 1
3 | (0) Old  Mem[x] | 
4 |  | (1) Mem[x]  New
5 | (1) New  Old + 1 | 
6 | (1) Mem[x]  New | 
Thread 1 Old = 0
Thread 2 Old = 0
Mem[x] = 1 after the sequence

## Slide 22: Purpose of Atomic Operations – To Ensure Good Outcomes
thread1:
thread2:
Old  Mem[x]
New  Old + 1
Mem[x]  New
Old  Mem[x]
New  Old + 1
Mem[x]  New
thread1:
thread2:
Old  Mem[x]
New  Old + 1
Mem[x]  New
Old  Mem[x]
New  Old + 1
Mem[x]  New
Or

## Slide 23: Atomic operations in cuda

## Slide 24: Data Race without Automic Operations
Both threads receive 0 in Old
Mem[x] becomes 1
thread1:
thread2:
Old  Mem[x]
New  Old + 1
Mem[x]  New
Old  Mem[x]
New  Old + 1
Mem[x]  New
Mem[x] initialized to 0
time

## Slide 25: Key Concepts of Atomic Operations
A read-modify-write operation performed by a single hardware instruction on a memory location address
  Read the old value, calculate a new value, and write the new value to the location
The hardware ensures that no other threads can perform another read-modify-write operation on the same location until the current atomic operation is complete
  Any other threads that attempt to perform an atomic operation on the same location will typically be held in a queue
  All threads perform their atomic operations serially on the same location

## Slide 26: Atomic Operations in CUDA
Performed by calling functions that are translated into single instructions (a.k.a. intrinsic functions or intrinsics)
  Atomic add, sub, inc, dec, min, max, exch (exchange), CAS (compare and swap)
  Read CUDA C programming Guide 4.0 or later for details
Atomic Add
  int atomicAdd(int* address, int val);
  reads the 32-bit word old from the location pointed to by address in global or shared memory, computes (old + val), and stores the result back to memory at the same address. The function returns old.

## Slide 27: More Atomic Adds in CUDA
Unsigned 32-bit integer atomic add
  unsigned int atomicAdd(unsigned int* address,
  unsigned int val);
Unsigned 64-bit integer atomic add
  unsigned long long int atomicAdd(unsigned long long
  int* address, unsigned long long int val);
Single-precision floating-point atomic add (capability > 2.0)
  float atomicAdd(float* address, float val);

## Slide 28: A Basic Text Histogram Kernel
The kernel receives a pointer to the input buffer of byte values
Each thread process the input in a strided pattern
__global__ void histo_kernel(unsigned char *buffer,
long size, unsigned int *histo)
{
int i = threadIdx.x + blockIdx.x * blockDim.x;
// stride is total number of threads
int stride = blockDim.x * gridDim.x;
// All threads handle blockDim.x * gridDim.x
// consecutive elements
while (i < size) {
int alphabet_position = buffer[i] – “a”;
if (alphabet_position >= 0 && alpha_position < 26)
atomicAdd(&(histo[alphabet_position/4]), 1);
i += stride;
}
}

## Slide 29: A Basic Histogram Kernel (cont.)
The kernel receives a pointer to the input buffer of byte values
Each thread process the input in a strided pattern
__global__ void histo_kernel(unsigned char *buffer,
long size, unsigned int *histo)
{
int i = threadIdx.x + blockIdx.x * blockDim.x;
// stride is total number of threads
int stride = blockDim.x * gridDim.x;
// All threads handle blockDim.x * gridDim.x
// consecutive elements
while (i < size) {
int alphabet_position = buffer[i] – “a”;
if (alphabet_position >= 0 && alpha_position < 26)
atomicAdd(&(histo[alphabet_position/4]), 1);
i += stride;
}
}

## Slide 30: Atomic operation performance

## Slide 31: Atomic Operations on Global Memory (DRAM)
An atomic operation on a DRAM location starts with a read, which has a latency of a few hundred cycles
The atomic operation ends with a write to the same location, with a latency of a few hundred cycles
During this whole time, no one else can access the location

## Slide 32: Atomic Operations on DRAM
Each Read-Modify-Write has two full memory access delays
  All atomic operations on the same variable (DRAM location) are serialized
atomic operation N
atomic operation N+1
time
DRAM read latency
DRAM read latency
DRAM write latency
DRAM write latency

## Slide 33: Latency determines throughput
Throughput of atomic operations on the same DRAM location is the rate at which the application can execute an atomic operation.
The rate for atomic operation on a particular location is limited by the total latency of the read-modify-write sequence, typically more than 1000 cycles for global memory (DRAM) locations.
This means that if many threads attempt to do atomic operation on the same location (contention), the memory throughput is reduced to < 1/1000 of the peak bandwidth of one memory channel!

## Slide 34: You may have a similar experience in supermarket checkout
Some customers realize that they missed an item after they started to check out
They run to the isle and get the item while the line waits
  The rate of checkout is drastically reduced due to the long latency of running to the isle and back.
Imagine a store where every customer starts the check out before they even fetch any of the items
  The rate of the checkout will be 1 / (entire shopping time of each customer)

## Slide 35: Hardware Improvements
Atomic operations on Fermi L2 cache
  Medium latency, about 1/10 of the DRAM latency
  Shared among all blocks
  “Free improvement” on Global Memory atomics
atomic operation N
atomic operation N+1
time
L2 latency
L2 latency
L2 latency
L2 latency

## Slide 36: Hardware Improvements
Atomic operations on Shared Memory
  Very short latency
  Private to each thread block
  Need algorithm work by programmers (more later)
..
atomic operation N
atomic operation N+1
time

## Slide 37: Privatization Technique for Improved Throughput

## Slide 38: Privatization
Atomic Updates
Heavy contention and serialization
Final Copy
…
Block 0
Block 1
Block N
Atomic Updates

## Slide 39: Privatization (cont.)
Final Copy
…
Block 0
Block 1
Block N
Atomic Updates
Copy 0
Copy 1
Final Copy
Copy N
…
Block 0
Block 1
Block N
…
Much less contention and serialization

## Slide 40: Privatization (cont.)
Final Copy
…
Block 0
Block 1
Block N
Atomic Updates
Copy 0
Copy 1
Final Copy
Copy N
…
Block 0
Block 1
Block N
…
Much less contention
and serialization

## Slide 41: Cost and Benefit of Privatization
Cost
  Overhead for creating and initializing private copies
  Overhead for accumulating the contents of private copies into the final copy
Benefit
  Much less contention and serialization in accessing both the private copies and the final copy
  The overall performance can often be improved more than 10x

## Slide 42: Shared Memory Atomics for Histogram
Each subset of threads are in the same block
Much higher throughput than DRAM (100x) or L2 (10x) atomics
Less contention – only threads in the same block can access a shared memory variable
This is a very important use case for shared memory!

## Slide 43: Shared Memory Atomics Requires Privatization
Create private copies of the histo[] array for each thread block
__global__ void histo_kernel(unsigned char *buffer,
long size, unsigned int *histo)
{
__shared__ unsigned int histo_private[7];

## Slide 44: Shared Memory Atomics Requires Privatization
Create private copies of the histo[] array for each thread block
__global__ void histo_kernel(unsigned char *buffer,
long size, unsigned int *histo)
{
__shared__ unsigned int histo_private[7];
if (threadIdx.x < 7) histo_private[threadidx.x] = 0;
__syncthreads();
Initialize the bin counters in the private copies of histo[]

## Slide 45: Build Private Histogram
int i = threadIdx.x + blockIdx.x * blockDim.x;
// stride is total number of threads
int stride = blockDim.x * gridDim.x;
while (i < size) {
atomicAdd( &(private_histo[buffer[i]/4), 1);
i += stride;
}

## Slide 46: Build Final Histogram
// wait for all other threads in the block to finish
__syncthreads();
if (threadIdx.x < 7) {
atomicAdd(&(histo[threadIdx.x]), private_histo[threadIdx.x] );
}
}

## Slide 47: More on Privatization
Privatization is a powerful and frequently used technique for parallelizing applications
The operation needs to be associative and commutative
  Histogram add operation is associative and commutative
  No privatization if the operation does not fit the requirement
The private histogram size needs to be small
  Fits into shared memory
What if the histogram is too large to privatize?
  Sometimes one can partially privatize an output histogram and use range testing to go to either global memory or shared memory