## Slide 1: The AMD gem5 APU simulator: Modeling gpus using the machine isa
Tony Gutierrez, Sooraj Puthoor, Tuan ta*, MatT Sinclair,
and brad beckmann
Amd research, *cornell
june 2, 2018

## Slide 2: Objectives and scope
Objectives
  Introduce the Radeon Open Compute Platform (ROCm)
  AMD’s Graphics Core Next (GCN) architecture and GCN3 ISA
  Describe the gem5-based APU simulator
Scope
  Emphasis on the GPU side of the simulator
    APU (CPU+GPU) model, not discrete GPU
    Covers GPU arch, GCN3 ISA, and HW-SW interfaces
Why are we releasing our code?
  Encourage AMD-relevant research
  Modeling ISA and real system stack is important [1]
  Enhance academic collaborations
    Enable intern candidates to get experience before arriving
    Enable interns to take their experience back to school
Acknowledgement
  AMD Research’s gem5 team
Modeling APU systems
[1] Gutierrez et al. Lost in Abstraction: Pitfalls of Analyzing GPUs at the Intermediate Language Level. HPCA, 2018.
Notes: APU simulator which tries to model the APU system
Capabilities of this simulator is the focus here
Capabilities plays a role in mapping
Acknowledge gem5 team

## Slide 3: Quick Survey
Who is in our audience?
  Graduate students
  Faculty members
  Working for government research labs
  Working for industry
Have you written an GPU program?
  CUDA, OpenCLTM, HIP, HC, C++ AMP, other languages
Have you used these simulators?
  GPGPU-Sim
  Multi2Sim
  gem5
    Our HSAIL-based APU model
Are you familiar with our HPCA 2018 paper?
  Lost in Abstraction: Pitfalls of Analyzing GPUs at the Intermediate Language Level

## Slide 4: Outline
Topic | Presenter | Time
Background | Tony | 8:00 – 8:15
ROCm, GCN3 ISA, and GPU Arch | Tony | 8:15 – 9:15
HSA Implementation in gem5 | Sooraj | 9:15 – 10:00
Break |  | 10:00 – 10:30
Ruby and GPU Protocol Tester | Tuan | 10:30 – 11:15
Demo and Workloads | Matt | 11:15 – 11:50
Summary and Questions | All | 11:50 – 12:00

## Slide 5: Background
Overview of gem5
  Source tree
GPU terminology and system overview
HSA standard and building blocks
  Coherent shared virtual memory
  User-level queues
  Signals
  etc.

## Slide 6: Overview of gem5
Open-source modular platform for system architecture research
  Integration of M5 (Univ. of Michigan) and GEMS (Univ. of Wisconsin)
  Actively used in academia and industry
Discrete-event simulation platform with numerous models
  CPU models at various performance/accuracy trade-off points
    Multiple ISAs: x86, ARM, Alpha, Power, SPARC, MIPS
  Two memory system models: Ruby and “classic” (M5)
    Including caches, DRAM controllers, interconnect, coherence protocols, etc.
  I/O devices: disk, Ethernet, video, etc.
  Full system or app-only (system-call emulation)
Cycle-level modeling (not “cycle accurate”)
  Accurate enough to capture first-order performance effects
  Flexible enough to allow prototyping new ideas reasonably quickly
See http://www.gem5.org
More information available from Jason Lowe-Power’s tutorial
  http://learning.gem5.org/tutorial/

## Slide 7: APU Simulator Code Organization
gem5
src
gpu-compute
mem/
protocol
mem/
ruby
configs
dev/
hsa
Gem5  top-level directory
  src/
    gpu-compute/  GPU core model
    mem/protocol/  APU memory model
    mem/ruby/  APU memory model
    dev/hsa/  HSA device models
  configs/
    example/  apu_se.py sample script
    ruby/  APU protocol configs
For more information about the configuration system, see Jason Lowe-Power’s tutorial.
For the remainder of this talk, files without a directory prefix are located in src/gpu-compute/

## Slide 8: GPU terminology
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
GPU
Core
L1D
GPU I-Cache
L2
CU
TCP
CU
TCP
CU
TCP
CU
TCP
SQC
TCC
SQC: Sequencer Cache (shared L1 instruction)
AMD terminology
CU: Compute Unit (SM in NVIDIA terminology)
TCP: Texture Cache per Pipe (private L1 data)
TCC: Texture Cache per Channel (shared L2)
Scalar Cache
Scalar Cache
Not shown (per GPU core):
LDS: Local Data Share (Shared memory in NVIDIA terminology, sometimes called “scratch pad”)
Notes: Clarifying AMD GPU terminology and what we use in these slides

## Slide 9: Example APU system
GPU + CPU core-Pair with a shared directory
CU
TCP
CU
TCP
CU
TCP
CU
TCP
SQC
TCC
CPU0
CPU1
CPU I-Cache
L1D
L1D
L2
Directory
Memory
Controller
Memory
GPU
CPU
Scalar Cache
Notes: Example of a APU system.
Notice the shared/private caches and the single directory structure

## Slide 10: AMD Terminology in a nutshell
Heterogeneous Systems Architecture (HSA) programming abstraction
  Standard for heterogeneous compute – supported by AMD hardware
  Light abstractions of parallel physical hardware
  Captures basic HSA and OpenCL constructs, plus much more
Grid: N-Dimensional (N = 1, 2, or 3) index space
  Partitioned into workgroups, wavefronts, and work-items
GPU Core
GPU Core
GPU
GPU Architecture
Workgroup
Workgroup
Grid
HSA Model
Wavefront (WF)
Work-item (WI)
Thread in CUDA
Grid in CUDA
Thread block in CUDA
Warp in CUDA
Grid
Workgroup
Work-item
Notes: Lightweight abstractions to physical hardware
Similar to OpenCL and much more
Division into workgroups, wavefronts and work-items

## Slide 11: Specification building blocks
HSA Hardware Building Blocks
Shared Virtual Memory
  Single address space
  Coherent
  Pageable
  Fast access from all components
  Can share pointers
Architected User-Level Queues
Signals
Platform Atomics
Defined Memory Model
Context Switching
HSA Software Building Blocks
HSA Runtime
  Implemented by the ROCm runtime
  Create queues
  Allocate memory
  Device discovery
Multiple high-level compilers
  CLANG/LLVM
  C++, HIP, OpenMP, OpenACC, Python
GCN3 Instruction Set Architecture
  Kernel state
  ISA encodings
  Program flow control
Industry specifications to enable existing programming languages to target the GPU
HSA Platform System Arch Specification
Industry standard, architected requirements for how devices share memory and communicate with each other
HSA System Runtime Specification
Open-Source
http://hsafoundation.com
http://github.com/HSAFoundation
Open-Source
GCN3 ISA
Specification
Open-Source

## Slide 12: APU Simulation Support
HSA Hardware Building Blocks
Shared virtual memory
  Single address space
  Coherent
  Fast access from all components
  Can share pointers
  Pageable
Architected user-level queues
  Via architected queuing language (AQL)
Signals
Platform atomics
Defined memory model
  Basic acquire and release operations
  Merging functional and timing models
Context switching
HSA Software Building Blocks
Radeon Open Compute platform (ROCm)
  AMD’s implementation of HSA principles
  Create queues
  Device discovery
  AQL support
  Allocate memory
Machine ISA
  GCN3
Heterogeneous Compute Compiler (HCC)
  CLANG/LLVM – direct to GCN3 ISA
  C++, C++ AMP, HIP, OpenMP, OpenACC, Python
Legend
Included in this release
Work-in-progress / may be released
Longer term work
  Acquire and release semantics as implemented by the compiler

## Slide 13: Outline
Topic | Presenter | Time
Background | Tony | 8:00 – 8:15
ROCm, GCN3 ISA, and GPU Arch | Tony | 8:15 – 9:15
HSA Implementation in gem5 | Sooraj | 9:15 – 10:00
Break |  | 10:00 – 10:30
Ruby and GPU Protocol Tester | Tuan | 10:30 – 11:15
Demo and Workloads | Matt | 11:15 – 11:50
Summary and Questions | All | 11:50 – 12:00

## Slide 14: Hw-sw interfaces
ROCm – high-level SW stack
HW-SW interfaces
Kernel launch flow
GCN3 ISA overview

## Slide 15: Are you ready to Rocm?
HCC
  Clang front end and LLVM-based backend
    Direct to ISA
    Multi-ISA binary (x86 + GCN3)
ROCm Stack
  HCC libraries
  Runtime layer – ROCr
  Thunk (user space driver) – ROCt
  Kernel fusion driver (KFD) – ROCk
GPU is a HW-SW co-designed machine
  Command processor (CP) HW aids in implementing HSA standard
  Rich application binary interface (ABI)
GPU directly executes GCN3 ISA
  Runtime ELF loaders for GCN3 binary
Sw stack and high-level simulation flow
HCC
MEM
CU
Application source
x86 ELF
GCN3 ELF +
Code metadata
ROCr
HCC
Libraries
ROCk
Command Processor
Hardware
GPU
ROCt
See https://rocm.github.io for documentation, source, and more.
User space
OS kernel space
Runtime loader loads GCN3 ELF into memory
shader.[hh|cc]
compute_unit.[hh|cc]
gpu_command_processor.[hh|cc]

## Slide 16: Detailed view of kernel launch
User space SW talks to GPU via ioctl()
  HCC/ROCr/ROCt are off-the-shelf ROCm
  ROCk is emulated in gem5
    Handles ioctl commands
CP frontend
  Two primary components:
    HSA packet processor (HSAPP)
    Workgroup dispatcher
Runtime creates soft HSA queues
  HSAPP maps them to hardware queues
  HSAPP schedules active queues
Runtime creates and enqueues AQL packets
  Packets include:
    Kernel resource requirements
    Kernel size
    Kernel code object pointer
    More…
Gpu frontend and hw-sw interface
MEM
CU
GPU
HSAPP
Dispatcher
HW Model Components
ROCk
User Space SW
ioctl()
gpu_compute_driver.[hh|cc]
dev/hsa/hsa_packet_processor.[hh|cc]
dev/hsa/hw_scheduler.[hh|cc]
CP
AQL
pkt
AQL
pkt
Head ptr
Tail ptr
HSA software queue
HW queue
HW Queue Scheduler
hsa_packet.hh
hsa_queue.hh
kernels
work-
groups

## Slide 17: Detailed view of kernel launch
Kernel dispatch is resource limited
  WGs are scheduled to CUs
Dispatcher tracks status of in-flight/pending kernels
  If a WG from a kernel cannot be scheduled, it is enqueued until resources become available
  When all WGs from a task have completed, the dispatcher frees CU resources and notifies the host
Dispatcher workgroup assignment
1) Try to dispatch WGs on every cycle
2) Pick oldest AQL pkt in queue; if it has unexecuted WGs, try to schedule them on a CU
3) Dispatch WG to CU if there are enough WF slots, enough GPRs, and enough LDS space
Shader
CU
CU
CU
GPU Dispatcher
AQL Pkt
AQL Pkt
-
HSA Queue Entry
(AQL kernel)
0
1
2
3
ID
AQL Pkt
Grid
wg(0, 0, 0)
wg(1, 0, 0)
wg(0, 1, 0)
wg(1, 1, 0)
dispatcher.[hh|cc]
hsa_queue_entry.hh

## Slide 18: Detailed view of kernel launch
ABI
  Interface between the application binary (ELF) and other components (e.g., OS, ISA, and HW)
  Function call convention, location of special values, etc.
ABI state primarily maintained in register file
  Some state maintained in the WF context for simplicity
CP responsible for initializing register file state
  Extracts metadata from code object (GPU ELF binary)
  Initializes both scalar and vector registers
  Kernel argument base address, vector condition codes (VCC), etc.
Gpu abi initialization
ABI
Binary
System software
HW/ISA
0x7fff…
…
CP
Register File
AMD Kernel Code
Kernel arguments base address
VCC HI
VCC LO
kernel_code.hh
# Load 2nd 64b kernel arg into s[2:3]
s_load_dwordx2 s[2:3], s[0:1], 0x08
GCN3 ISA application loading a kernel argument

## Slide 19: Gpu microarchitecture
High-level gem5 and Ruby core models
gem5 ISA/HW separation
  Object oriented design
    Modular, extensible…
    Possible to support multiple-ISAs
GCN microarchitecture
gem5’s conceptual pipeline and timing flow
GCN3 ISA description
gem5 compute unit implementation
  Pipeline breakdown

## Slide 20: GPU CORE MODULES
GPU core is the compute unit
  Resources inside GPU Core
    Instruction buffering, Registers, Vector ALUs
  Resources outside GPU Core
    TCP, TCC, SQC (Ruby based)
Shader: object containing all GPU core models
  The top-level view of the GPU in gem5
  Contains multiple CUs
  With other miscellaneous components
GPU CORE MODULES vs. RUBY MODULES
CU
TCP
CU
TCP
CU
TCP
CU
TCP
SQC
TCC
Hardware building blocks
GPU Core
Modules
APU
Simulator
Ruby
Modules
Simulator software modules
Scalar Cache

## Slide 21: Isa description/microarchitecture separation
GPUStaticInst & GPUDynInst
  Architecture-specific code src/arch/
    Base instruction classes
    ISA decoder
    ISA state, etc.
  Define API for instruction execution
    e.g., execute() – perform instruction execution
  Implemented by ISA-specific instruction classes
GPUExecContext & GPUISA
  Define API for accessing ISA state
Object-oriented design
  Base classes define the API
  Model uses base class pointers
  Configuration system instantiates ISA-specific objects
GPU core model components
ISA specific instruction classes and methods
Wavefront related interfaces
Static instruction objects
HW Blocks
Instruction and ISA specific classes
Dynamic instruction information and interfaces
Shader
Compute Units
WF Context
GCN3 Static Inst
GCN3 Decoder
Operands
ISA State
ISA Registers
GPUStaticInst
GPUDynInst
GPUExecContext
GPU core state
ISA-specific state
GPU Core/ISA API definition
gpu_exec_context.[hh|cc]
gpu_dyn_inst.[hh|cc]
src/arch/gcn3/gpu_static_inst.hh|cc]
src/arch/gcn3/gpu_isa.hh, src/arch/gcn3/isa.cc
src/arch/gcn3/operand.hh
src/arch/gcn3/registers.[hh|cc]
Relevant source:
Notes: Explain gpustaticinst
Explain why the wavefront interface is important

## Slide 22: GPU Core BASED on GCN ARCHITECTURE
More details available here: GCN Architecture Whitepaper www.amd.com/Documents/GCN_Architecture_whitepaper.pdf
wavefront.[hh|cc]
lds_state.[hh|cc]
arch/gcn3/gpu_decoder.hh
arch/gcn3/decoder.cc
Instruction Fetch
SIMD 2
PC & IB
10 WFs
Instruction Arbitration
Execute
Compute Unit
VALU
VALU
VALU
VALU
SIMDs
Scalar Unit
Scalar RF
Vector RF
Local Data Share Mem
Message & Branch Unit
SIMD 3
PC & IB
10 WFs
SIMD 0
PC & IB
10 WFs
SIMD 1
PC & IB
10 WFs
Export/GDS Decode
Vector Mem Decode
Scalar Decode
LDS Decode
Vector Decode
TCP
SQC
TCC
Scalar
Cache
src/mem/protocol/GPU_VIPER-TCP.sm
src/mem/protocol/GPU_VIPER-TCC.sm
src/mem/protocol/GPU_VIPER-SQC.sm
scalar_register_file.[hh|cc]
vector_register_file.[hh|cc]
Notes: One comment is keep names consistent

## Slide 23: GPU CORE Timing
Execute-in-execute philosophy
Pipeline stages
  Fetch: fetch for dispatched WFs - fetch_stage.[hh|cc] and fetch_unit.[hh|cc]
  Scoreboard: Check which WFs are ready - scoreboard_check_stage.[hh|cc]
  Schedule: Select a WF from the ready pool - schedule_stage.[hh|cc]
  Execute: Run WF on execution resource - exec_stage.[hh|cc]
  Memory pipeline: Execute LDS/global memory operation
    local_memory_pipeline.[hh|cc]
    global_memory_pipeline.[hh|cc]
    scalar_memory_pipeline.[hh|cc]
CONCEPTUAL TIMING STAGES
Fetch
Scoreboard
Execute
Schedule
Memory pipeline
Fetched WFs
Ready WFs
Executing WFs
Local memory (LDS)
Global memory (TCP)
Scalar memory
Notes: These are not pipeline stages
If not in a pipeline fashion then how are we keeping track of timing
Is the cost of moving between queues zero (how is this implemented in hardware)
Capability vs. accuracy tradeoff

## Slide 24: Gcn3 gpu isa
Vector and scalar instructions
  Single instruction stream
  Not really “SIMT”
  Divergence handled by scalar unit
    Can directly modify execution mask
    Jump over basic blocks when EXEC = 0
Instructions broken down by OP type
  Op types map to different functional units in CU
  The CU can issue one instruction to each unit in the same cycle
    Export/GDS not supported in gem5
Op Type | Functional Unit | Usage
SOPP | Branch/Message Unit | Branching, NOPs, Barriers, waitcnts, messaging
SOPC/SOPK/SOP1/SOP2 | Scalar ALU | General scalar computation/divergence handling
SMEM | Scalar Memory | Scalar memory access, cache maintenance
VOPC/VOP1/VOP2/VOP3 | SIMD Unit | General SIMD computation
DS | LDS | Private scratch pad memory
MUBUF | Vector Memory | Accessing vector memory, cache maintenance
FLAT | LDS/Vector Memory | Accessing vector memory, may resolve to LDS or system memory
VINTRP/MTBUF/MIMG/EXP | Varies | Primarily used by graphics. Not currently modeled in gem5; however, the infrastructure to do so is present.
Full GCN3 spec available at: https://gpuopen.com/compute-product/amd-gcn3-isa-architecture-manual/
arch/gcn3/insts/op_encodings.[hh|cc]
arch/gcn3/insts/instructions.[hh|cc]

## Slide 25: GPU Core MODULE INTERNALS
Compute unit
  Four 16-wide SIMD units
  SIMD hosts WFs
  Private resources to each SIMD
    Instruction buffering
    Registers
    Vector ALUs
  Shared resources
    Fetch and decode
    TCP
    LDS
SHARED vs. PRIVATE STRUCTURES
CU
TCP
CU
TCP
CU
TCP
CU
TCP
SQC
TCC
Scalar Cache
Instruction Fetch
WF 0-9 Contexts
WF 10-19 Contexts
WF 20-29 Contexts
WF 30-39 Contexts
Instruction Decode/Arbitration
SIMD 0
VGPRs
Vector ALU
SIMD 1
VGPRs
Vector ALU
SIMD 2
VGPRs
Vector ALU
SIMD 3
VGPRs
Vector ALU
TCP
LDS
Scalar Unit
SGPRs
Integer ALU
Branch Unit
4-CU-shared SQC

## Slide 26: Fetch and Wavefront contexts
SQC shared by 4 CUs
  Number of SQCs and CUs are configurable
Fetch
  Shared and arbitrated between SIMDs in a CU
  Fetch to each SIMD unit
  Buffers fetched cache lines per WF
WF Contexts
  10 WFs per SIMD, 40 per CU
    PC and decoded instruction buffers (IB)
    Register file and LDS allocation
  ¼ of WF executes each cycle
    4 cycles needed to fully execute single SIMD instruction
PC
IB
WF 0
PC
IB
WF 1
PC
IB
WF 9
Fetch buffer
(per WF)
4-CU-shared SQC
Instruction Fetch
WF 0-9 Contexts
WF 10-19 Contexts
WF 20-29 Contexts
WF 30-39 Contexts
Instruction Decode/Arbitration
SIMD 0
VGPRs
Vector ALU
SIMD 1
VGPRs
Vector ALU
SIMD 2
VGPRs
Vector ALU
SIMD 3
VGPRs
Vector ALU
TCP
LDS
Scalar Unit
SGPRs
Integer ALU
Branch
Unit
wavefront.[hh|cc]
PC0
Instruction Data
PC1
Instruction Data
fetch_stage.[hh|cc]
fetch_unit.[hh|cc]

## Slide 27: Decode and issue
Instructions are decoded out of fetch buffers
Instruction arbitration
  Can issue to each functional unit each cycle
  Finds ready WFs
  Scheduling policy dictates which WFs have priority
    Oldest first, easy to add others
Fetch buffer
(per WF)
4-CU-shared SQC
Instruction Fetch
WF 0-9 Contexts
WF 10-19 Contexts
WF 20-29 Contexts
WF 30-39 Contexts
Instruction Decode/Arbitration
SIMD 0
VGPRs
Vector ALU
SIMD 1
VGPRs
Vector ALU
SIMD 2
VGPRs
Vector ALU
SIMD 3
VGPRs
Vector ALU
TCP
LDS
Scalar Unit
SGPRs
Integer ALU
Branch
Unit
scoreboard_check_stage.[hh|cc]
LDS
SIMD
Scalar
Global Mem
WF Contexts
Scoreboard
Ready List Per Execution Unit
schedule_stage.[hh|cc]
Read Operands
WF Arbitration
LDS
SIMD
Scalar
Global Mem
Execution Units
IB
Instruction data decoded into instruction buffer
scheduler.[hh|cc]
scheduling_policy.hh

## Slide 28: Register files
4-CU-shared SQC
Instruction Fetch
WF 0-9 Contexts
WF 10-19 Contexts
WF 20-29 Contexts
WF 30-39 Contexts
Instruction Decode/Arbitration
SIMD 0
VGPRs
Vector ALU
SIMD 1
VGPRs
Vector ALU
SIMD 2
VGPRs
Vector ALU
SIMD 3
VGPRs
Vector ALU
TCP
LDS
Scalar Unit
SGPRs
Integer ALU
Branch
Unit
General Purpose Registers (GPRs)
  Vector registers (VGPR) partitioned per SIMD
    Configurable size
    Because each SIMD executes independent WF
  32-bit wide
    Combine adjacent VGPRs for 64-bit or 128-bit data
  Each WF also has scalar general purpose registers (SGPRs)
Register Allocation Done by a Simple Pool Manager
  Only allows one WG at a time
  Statically mapped virtual  physical register index
    <base, limit> pair of registers specify GPR allocation
  Modular design – more advanced pool managers can be swapped into the VRF seamlessly
  Simple timing model with constant delay
V0
VN-1
VN
VN+1
VN+2
WF0 – <V0, N>
SIMD 0
This is an area where gem5 user contributions would be extremely valuable.
vector_register_file.[hh|cc]
scalar_register_file.[hh|cc]
simple_pool_manager.[hh|cc]
static_register_manager_policy.[hh|cc]

## Slide 29: Vector ALUs
4-CU-shared SQC
Instruction Fetch
WF 0-9 Contexts
WF 10-19 Contexts
WF 20-29 Contexts
WF 30-39 Contexts
Instruction Decode/Arbitration
SIMD 0
VGPRs
Vector ALU
SIMD 1
VGPRs
Vector ALU
SIMD 2
VGPRs
Vector ALU
SIMD 3
VGPRs
Vector ALU
TCP
LDS
Scalar Unit
SGPRs
Integer ALU
Branch
Unit
16-lane vector pipeline per SIMD
  Each lane has a set of functional units
  One work-item per lane
4 cycles to execute a WF for all 64 work-items
  In gem5, 64 work-items are executed in one tick and ticks are multiplied by 4
SIMD execution may take longer if work-items in WF have dissimilar behaviors
  Example 1: Branch (or spatial) divergence
    Branches executed through predication
    When control flow diverges, all lanes take all paths
  Example 2: Memory (or temporal) divergence
    Longer access latency by one work-item stalls entire WF
Vector ALU in SIMD
Lane 0
Lane 1
Lane 15
compute_unit.[hh|cc]

## Slide 30: GPU CORE TIMING
Memory instructions generate memory requests
  Part of GPU instruction definition (ISA-specific)
Three phases
  execute()
    Read operands, calculate address, increment wait count, and issue to appropriate memory pipe
  initiateAcc()
    Issue request to memory system
  completeAcc()
    For loads write back data. Stores do nothing.
New machine ISAs can use this capability to support their own memory instructions
Individual stages contribute to the memory instruction timing
  Additionally memory end timing handled by Ruby and memory technology parameters
Memory dependencies are preserved using waitcnts
Handling Memory INSTRUCTIONS
GPU dynamic memory instruction
Create packet
Global/LDS operation
Writeback
Increment waitcnt
flat_load_dword v4, v[4:5]
flat_load_dword v16, v[8:9]
flat_load_dword v23, v[14:15]
flat_load_dword v10, v[10:11]
s_waitcnt cnt(3)
v_ashrrev v5, 31, v4
Example GCN3 code:
flat_load writes v4
Waitcnt specifies wait count value must be ≤ 3
Arithmetic shift later reads from v4
Waitcnt waits until at least #1 is finished
1
2
3
gpu_dyn_inst.[hh|cc]
arch/gcn3/instructions.[hh|cc]
arch/gcn3/insts/op_encodings[hh|cc]
local_memory_pipeline.[hh|cc]
global_memory_pipeline.[hh|cc]
scalar_memory_pipeline.[hh|cc]

## Slide 31: Vector memory execution
4-CU-shared SQC
Instruction Fetch
WF 0-9 Contexts
WF 10-19 Contexts
WF 20-29 Contexts
WF 30-39 Contexts
Instruction Decode/Arbitration
SIMD 0
VGPRs
Vector ALU
SIMD 1
VGPRs
Vector ALU
SIMD 2
VGPRs
Vector ALU
SIMD 3
Vector Registers
Vector ALU
TCP
LDS
Scalar Unit
Scalar Registers
Integer ALU
Branch
Unit
In gem5:
  Address calculation: arch/gcn3/insts/op_encodings.hh
  Address coalescing
    mem/ruby/system/GPUCoalescer.[hh|cc]
    mem/ruby/system/VIPERCoalescer.[hh|cc]
    mem/protocol/GPU_VIPER-TCP.sm
    mem/protocol/GPU_VIPER-TCC.sm
LDS
  User-managed address space
  Scratchpad for WFs in workgroup
  Used for data sharing and synchronization within workgroup
  Cleared when workgroup completes
  In gem5, functional model with a pointer per workgroup
Coalescer
Tag
Data
TCP
Address
Write data
Read data
To shared TCC
TCC

## Slide 32: Control flow divergence
simt vs. vector execution model
cmp_lt $c0, $s0, 32
cbr $c0, @BB2
ret
cmp_gt $c0, $s0, 15
cbr $c0, @BB4
st 84, [$d0]
br @BB4
st 90, $[d0]
BB0
BB1
BB3
BB2
BB4
Source code:
if (i > 31) {
*x = 84;
} else if (i < 16) {
*x = 90;
}
Execute taken path first & flush IB
Fall through to BB3
Instruction buffer
cmp
st
cbr
br
cmp
st
cbr
ret
st
br
ret
ret
Reconvergence point reached, HW initiated jump to divergent path
Branch over BB2 & BB3, flush IB
HSAIL
Flushed!
Flushed!
Flushed!

## Slide 33: Control flow divergence
simt vs. vector execution model
cmp_lt $c0, $s0, 32
cbr $c0, @BB2
ret
cmp_gt $c0, $s0, 15
cbr $c0, @BB4
st 84, [$d0]
br @BB4
st 90, $[d0]
BB0
BB1
BB3
BB2
BB4
Instruction buffer
cmp_le vcc, 32, v0
s_load s[0:1], s[6:7], 0x0
s_and_saveexec s[2:3], vcc
v_mov v0, 0x00000054
s_cbranch_execz @BB2
s_endpgm
s_waitcnt lgkmcnt(0)
v_mov v[1:2], s[0:1]
flat_store v[1:2], v0
s_waitcnt lgkmcnt(0)
v_mov v[1:2], s[0:1]
flat_store v[1:2], v0
s_andn2 exec, s[2:3], exec
s_cbranch_execz @BB5
v_cmp_ge vcc, 15, v0
s_and_saveexec s[4:5], vcc
v_mov v0, 0x0000005a
s_cbranch_execz @BB5
BB0
BB1
BB2
BB3
BB4
BB5
Branches are optimizations for case when EXEC = 0 for a BB
cmp
s_load
s_and_saveexec
v_mov
HSAIL
GCN3
Source code:
if (i > 31) {
*x = 84;
} else if (i < 16) {
*x = 90;
}

## Slide 34: Outline
Topic | Presenter | Time
Background | Tony | 8:00 – 8:15
ROCm, GCN3 ISA, and GPU Arch | Tony | 8:15 – 9:15
HSA Implementation in gem5 | Sooraj | 9:15 – 10:00
Break |  | 10:00 – 10:30
Ruby and GPU Protocol Tester | Tuan | 10:30 – 11:15
Demo and Workloads | Matt | 11:15 – 11:50
Summary and Questions | All | 11:50 – 12:00

## Slide 35: What is HSA?
Processor design that makes it easy to harness the entire computing power of GPUs for faster and more power-efficient devices, including personal computers, tablets, smartphones, and servers
Bringing GPU performance to a wide variety of applications
Heterogeneous System Architecture

## Slide 36: Key features of hsa
hComm
Heterogeneous Communication via Signals and Atomics
hQ
Heterogeneous Queuing
hUMA
Heterogeneous Unified Memory Architecture

## Slide 37: Traditional discrete gpu
Separate memory
Separate addr space
  No pointer-based data structures
Explicit data copying
  High latency
  Low bandwidth
Need lots of compute on GPU to amortize copy overhead
Very limited GPU memory capacity
GPU Memory
CU
1
…
CU
2
CU
3
CU
M
Coherent System Memory
CPU
1
CPU
N
…
CPU
2
PCIe™

## Slide 38: hUMA unified memory
Unified address space
  GPU uses user virtual addresses
  Fully coherent
No explicit copying
  Data movement on demand
Pointer-based data structures shared across CPU & GPU
Pageable virtual addresses
  No GPU capacity constraints
Unified Coherent Memory
CPU
1
CPU
N
…
CPU
2
CU
1
…
CU
2
CU
3
CU
M

## Slide 39: HSA Atomics
Atomic memory updates fundamental to efficient thread synchronization
  Implement primitives like mutexes, semaphores, histograms, …, previously only implemented on CPU
HSA supports 32bit or 64bit values for atomic ops
  CAS, SWAP, add, increment, sub, decrement, …
  and other common arithmetic and logic atomic ops
On PCI-Express system, atomics map to PCI-E atomics
HSA specifies a well-defined “SC for HRF” memory model
  A variant of “Release Consistency” model
  Acquire: pull latest data (to me)
  Release: push latest data (to others)
  Compatible with C++11, Java, OpenCL, and .NET memory models
  Details: “HSA Platform System Arch Specification”, http://hsafoundation.com
Notes: Picture Source: Wikimedia commons

## Slide 40: The HSA Signals Infrastructure
Hardware-assisted signaling and synchronization primitives
  Memory semantics, equivalent to atomics
    e.g., 32bit or 64bit value, content updated atomically
    Threads can wait on a value
  Power-efficient synchronization between CPU and GPU threads
Allows one-to-one, many-to-one, and one-to-many signaling
  Used by system software, runtime, and application SW
  Infrastructure to build higher-level synchronization primitives like mutexes, semaphores, etc.
Updating the value of a signal is equivalent to sending the signal
  Release semantics: push data to others
Waiting on a signal is also permitted
  Via a wait instruction or via a runtime API
  Acquire semantics: pull data from others
Notes: Source: wikimedia commons

## Slide 41: Traditional Command and Dispatch Flow
Soft Queue
Kernel Mode Driver
App A
User Mode Driver
Direct3D
Soft Queue
Kernel Mode Driver
App C
User Mode Driver
Direct3D
Soft Queue
Kernel Mode Driver
App B
User Mode Driver
Direct3D
Task Queue
A
GPU
C
B
A
B

## Slide 42: hQ Command and Dispatch Flow
C
User-mode application talks directly to the hardware
  HSA Architected Queuing Language (AQL) defines vendor-independent format
  No system call
  No kernel driver involvement
Hardware scheduling
Greatly reduced dispatch overhead  less overhead to amortize  profitable to offload smaller tasks
Device enqueue: GPU kernels can self-enqueue additional tasks (dynamic parallelism)
App C
App B
App A
GPU
C
C
B
B
B
A
A
A
A
A

## Slide 43: Native Support for data-Dependent tasks
Expose Directed Acyclic Graphs (DAG) to Hardware
Barrier Packet
Completion Signal A
Completion Signal B
C
BP
B
A
head
head
head
HSA Queues
Task A
Task B
Task C
GPU hardware is responsible for managing and scheduling tasks (No Operating System!)

## Slide 44: Command queue oversubscription challenge
Sooraj Puthoor, Xulong Tang, Joseph Gross, and Bradford M. Beckmann. 2018. Oversubscribed Command Queues in GPUs. In Proceedings of the 11th Workshop on General Purpose GPUs (GPGPU-11). February 2018.
HW Queues
HSA Queues (QID = 0)
HSA Queues (QID = 1)
Task: A
Task: B
Barrier Pkt
Task: D
HSA Queues (QID = 2)
HSA Queues (QID = 3)
Barrier Pkt
Task: C
HSA Queues (QID = 0)
HSA Queues (QID = 1)
Task: B
Task: A
Barrier Pkt
Task: D
HSA Queues (QID = 2)
HSA Queues (QID = 3)
Barrier Pkt
Task: C
A
C
D
B

## Slide 45: Queue scheduling hardware
Component | Source file
driver | gpu-compute/gpu_compute_driver.cc dev/hsa/kfd_ioctl.h
hardware scheduler | dev/hsa/hw_scheduler.[hh¦cc]
packet processor | dev/hsa/hsa_packet_processor.[hh¦cc]
dispatcher | gpu-compute/dispatcher.[hh¦cc]
HW Model Components
ROCk
User Space SW
ioctl()
CU
GPU
HSAPP
Dispatcher
CP
HW queue
HW Queue Scheduler
work-
groups
CPU
Memory
HSA software queue #0
HSA software queue #1
Active list
*Q0
*Q1
*Q2
Registered list
Q0
Q2
gem5 maintains active list inside HW queue scheduler

## Slide 46: Doorbell pages and event pages
HW Model Components
ROCk
User Space SW
ioctl()
AQL
pkt
AQL
pkt
Head ptr
Tail ptr
HSA software queue
CU
GPU
HSAPP
Dispatcher
CP
HW queue
HW Queue Scheduler
work-
groups
CPU
Memory
HSADriver::mmap(mmap args)
runtime calls mmap on the driver
mmap offset distinguishes event page vs doorbell page mmap
2. driver allocates doorbell page and returns the page address
For doorbells -> Driver maps the page address to PIO address in the PT
For events -> Event pages are user pages
3. runtime allocates doorbell address for each queue based on queue ID.
Event pages are currently unused; model relies on functional interfaces for event notification.

## Slide 47: HSA Queue creation
1. hsa_queue_create(some args)
2. GPUComputeDriver::ioctl(tc, AMDKFD_IOC_CREATE_QUEUE)
3. HWScheduler::registerNewQueue(some args)
HW Model Components
ROCk
User Space SW
ioctl()
AQL
pkt
AQL
pkt
Head ptr
Tail ptr
HSA software queue
CU
GPU
HSAPP
Dispatcher
CP
HW queue
HW Queue Scheduler
work-
groups
CPU
Memory

## Slide 48
QUEUE swapping logic
// Wakeup every wakeupDelay ticks
1. HWScheduler::wakeup()
2. HWScheduler::contextSwitchQ ()
registered list (Packet processor)
active list (Hardware scheduler)
HW Model Components
ROCk
User Space SW
ioctl()
AQL
pkt
AQL
pkt
Head ptr
Tail ptr
HSA software queue
CU
GPU
HSAPP
Dispatcher
CP
HW queue
HW Queue Scheduler
work-
groups
CPU
Memory

## Slide 49
Hsa signal Creation
1. hsa_signal_create(some args)
2. GPUComputeDriver::ioctl(tc, AMDKFD_IOC_CREATE_EVENT)
3. hsa_signal_wait_scacquire(some args)
4. GPUComputeDriver::ioctl(tc, AMDKFD_IOC_WAIT_EVENTS)
5. GPUComputeDriver::ioctl(tc, AMDKFD_IOC_SET_EVENT) //or
5. signalWakeupEvent(event ID)
HW Model Components
ROCk
User Space SW
ioctl()
AQL
pkt
AQL
pkt
Head ptr
Tail ptr
HSA software queue
CU
GPU
HSAPP
Dispatcher
CP
HW queue
HW Queue Scheduler
work-
groups
CPU
Memory

## Slide 50
Hsa doorbells
1. hsa_signal_store_screlease(queue->doorbell_signal, packet_id);
2. HSAPacketProcessor::write(some args)
3. HWScheduler::write(Addr db_addr, uint32_t doorbell_reg)
4. HSAPacketProcessor::getCommandsFromHost(some args)
HW Model Components
ROCk
User Space SW
ioctl()
AQL
pkt
AQL
pkt
Head ptr
Tail ptr
HSA software queue
CU
GPU
HSAPP
Dispatcher
CP
HW queue
HW Queue Scheduler
work-
groups
CPU
Memory

## Slide 51: Outline
Topic | Presenter | Time
Background | Tony | 8:00 – 8:15
ROCm, GCN3 ISA, and GPU Arch | Tony | 8:15 – 9:15
HSA Implementation in gem5 | Sooraj | 9:15 – 10:00
Break |  | 10:00 – 10:30
Ruby and GPU Protocol Tester | Tuan | 10:30 – 11:15
Demo and Workloads | Matt | 11:15 – 11:50
Summary and Questions | All | 11:50 – 12:00

## Slide 52: Outline
Topic | Presenter | Time
Background | Tony | 8:00 – 8:15
ROCm, GCN3 ISA, and GPU Arch | Tony | 8:15 – 9:15
HSA Implementation in gem5 | Sooraj | 9:15 – 10:00
Break |  | 10:00 – 10:30
Ruby and GPU Protocol Tester | Tuan | 10:30 – 11:15
Demo and Workloads | Matt | 11:15 – 11:50
Summary and Questions | All | 11:50 – 12:00

## Slide 53: Ruby memory contributions
Ruby Background
CU – Memory Interface
GPU VIPER Protocol
GPU SLICC Protocol Tester
Outline

## Slide 54: Ruby memory contributions
Ruby Background
CU – Memory Interface
GPU VIPER Protocol
GPU SLICC Protocol Tester
Outline

## Slide 55: Ruby background
Flexible Memory System
  Rich configuration
    Simulate combination of caches, coherence, interconnect, etc.
  Rapid prototyping
    Domain-Specific Language (SLICC) for coherence protocols
    Modular components
Detailed statistics
  Latency distributions for requests
  Generated state transitions, network utilization, etc.
Detailed component simulation
  Network (fixed/flexible Garnet pipelines and simple)
  Caches (pluggable replacement policies)
  Memory (shared memory controllers between Classic and Ruby)
gem5 Ruby tutorial: http://learning.gem5.org/book/part3/index.html
Our GCN3 GPU model only works with Ruby memory

## Slide 56: Ruby memory contributions
Ruby Background
CU – Memory Interface
GPU VIPER Protocol
GPU SLICC Protocol Tester
Outline

## Slide 57: CU - Memory interface
Scalar memory operations (to scalar cache)
  S_LOAD
  S_STORE
Vector memory operations (to TCP)
  BUFFER_LOAD
  BUFFER_STORE
  BUFFER_ATOMIC
Cache-wide Synchronization Operation
  BUFFER_WBINVL1: write back and invalidate TCP cache
Primary GCN3 memory operations

## Slide 58: CU - Memory interface
GPU Memory Coalescing – Critical For Performance
CU
TCP
Coalescer
…
…
CU-side memory ports
Coalescer-side memory ports
Byte-aligned request/response memory packets
coalescePacket
Coalesced Table
Mandatory Queue
Cache callbacks
(e.g., readCallback, writeCallback)
Uncoalesced Table
makeRequest
issueRequest
Cache-line-aligned Ruby requests
completeHitCallback
hitCallback
Only coalesces packets from the same wavefront

## Slide 59: Ruby memory contributions
Ruby Background
CU – Memory Interface
GPU VIPER Protocol
GPU SLICC Protocol Tester
Outline

## Slide 60: GPU VIPER protocol (see src/mem/protocol)
High-level structure
CU
TCP
CU
TCP
CU
TCP
CU
TCP
SQC (Inst)
TCC
CPU0
CPU1
L1I
L1D
L1D
L2
Stateless
Directory
Memory
Controller
Memory
GPU
CPU
MOESI_AMD_Base-dir.sm
GPU_VIPER-SQC.sm
GPU_VIPER-TCP.sm
GPU_VIPER-TCC.sm
MOESI_AMD_Base-CorePair.sm
SQC (Scalar)
Notes: Example of a APU system.
Notice the shared/private caches and the single directory structure

## Slide 61: GPU Viper protocol
GPU write-through protocol
  Store & Atomic requests are written through TCP and TCC
  TCP performs Store & Atomic requests immediately (i.e., no stalling for exclusive permissions)
  For Store requests, TCP calls back immediately (i.e., writeCallback) without waiting for ACKs from memory
  TCP does another callback (i.e., writeCompleteCallback) when receiving store-complete ACKs from memory
  Atomic requests are performed in memory
Data coherence in TCP
  TCP-INV requests (e.g., issued by BUFFER_WBINVL1) to invalidate entire TCP
Data coherence between TCC and CPU caches
  Data coherence is maintained through a stateless directory (MOESI_AMD_Base-dir.sm)
Support single coherent address space between CPU and GPU
Write-through coherence
Notes: Image from https://openclipart.org/detail/99781/snake
License: https://openclipart.org/unlimited-commercial-use-clipart

## Slide 62: GPU Viper protocol
Release consistency
  Hower et al. [ASPLOS 2014]
  HSA System Arch Specification [hsafoundation.com]
Acquire fence
  Issue TCP-INV to invalidate all stale data in TCP
Release fence
  Wait for all outstanding store requests to commit globally (i.e., writeCompleteCallback)
  Wait for all atomic requests (i.e., atomicCallback)
Release consistency support
Notes: Image from https://openclipart.org/detail/99781/snake
License: https://openclipart.org/unlimited-commercial-use-clipart

## Slide 63: Ruby memory contributions
Ruby Background
CU – Memory Interface
GPU VIPER Protocol
GPU SLICC Protocol Tester
Outline

## Slide 64: GPU slicc protocol tester
Developing a functionally correct SLICC protocol is challenging
We need an effective tool to verify a protocol
Motivation
Desired Features | GPU Protocol Tester
GPU protocol compatibility | 
Precise validation | 
Wide bug coverage | 
Fast bug detection | 
Intuitive bug report | 
Notes: Developing a correct SLICC protocol is challenging because of many states, transitions, events and possible deadlocks
GPU protocol compatibility – software cache coherence & release consistency
Precise validation – if the tester is doing a LD, it should know exactly what the LD is going to return.
Wide bug coverage
  No atomic
  No false sharing
  No GPU-like throughput stress – wavefront issues 1 request at a time
Fast bug detection – less effective if I can’t cover many bugs
Intuitive bug report – No precise validation -> hard to trace what transactions are related to my failure

## Slide 65: GPU slicc protocol tester
High-level structure – ruby interface
CPU core
GPU core
Sequencer
Sequencer
Sequencer
Coalescer
CPU Inst$
CPU Data$
GPU Inst$
GPU Data$
The rest of cache hierarchy and memory
Ruby Ports
Ruby Memory
Compute Cores
Sequencer
GPU Scalar$

## Slide 66: GPU slicc protocol tester
High-level structure – ruby interface
CPU Tester Thread
GPU Tester Wavefront
Sequencer
Sequencer
Sequencer
Coalescer
CPU Inst$
CPU Data$
GPU Inst$
GPU Data$
The rest of cache hierarchy and memory
Ruby Ports
Ruby Memory
Protocol Tester
Sequencer
GPU Scalar$
Only support data caches for now

## Slide 67: GPU slicc protocol tester
Issue sequences (a.k.a., episodes) of memory operations (i.e., Load, Store, Atomic and synchronization operations) with respect to release consistency
CPU tester thread
  Load, Store, and Atomic operations are scalar
  Acquire and release fence are no-ops
GPU Tester Wavefront
  Load, Store, and Atomic are vector operations (i.e., issued by multiple lanes in a wavefront)
  Acquire fence issues TCP-INV
  Release fence waits for all outstanding Store and Atomic operations to complete (i.e., through writeCompleteCallback and atomicCallback)
High-level structure – Tester thread

## Slide 68: GPU slicc protocol tester
High-level structure - episode
Think of an episode as a critical section
Acquire Lock
Mix of LDs & STs
Release Lock
ATOMIC (A)
ACQUIRE
LD (X)
ST (Y)
…
ATOMIC (A)
RELEASE
CPU Tester Thread
AT (A0)
ACQUIRE
LD (X0)
…
RELEASE
GPU Tester Wavefront (4 lanes)
AT (A1)
AT (A2)
LD (X1)
LD (X2)
ST (Y0)
ST (Y1)
ST (Y2)
AT (A0)
AT (A1)
AT (A2)
AT (A3)
LD (X3)
ST (Y3)
AT (A3)

## Slide 69: GPU slicc protocol tester
High-level structure - Execution flow per thread
Issue a new episode
Execute the episode
Retire the episode
Randomly generate a series of Load, Store and Atomic operations to be issued
For Stores, reserve variables
Issue requests across all lanes
Check dependencies between requests
Receive and validate data responses (for Load and Atomic operations)
Track per-address last writers after each store operation
Release all reserved variables in this episode
Check for completion

## Slide 70: GPU slicc protocol tester
Random GPU Ruby tester does NOT cover data-race scenarios
Data race free (drf) request stream
Atomic_Acq (A)
LD (X) = 0
ST: 1 -> Y
Atomic_Rel (A)
Atomic_Acq (A)
LD (Y) = 0 or 1?
ST: 2 -> X
Atomic_Rel (A)
Atomic_Acq (A)
LD (Y) = 1
ST: 1 -> X
Atomic_Rel (A)
Time
race
no race
A: Atomic variable
X & Y: Non-atomic variables associated with A
happened-before
Eps 0
Eps 1 (Invalid)
Eps 2
Notes: If data stream in eps 1 was generated, what would the value returned in LD(X) and LD(Y)

## Slide 71: GPU slicc protocol tester
High level structure – address range
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0x00 | 0x04 | 0x08 | 0x0c | 0x10 | 0x14 | 0x18 | 0x1c | 0x20 | 0x24
Variables
Addresses
Randomly mapped
Atomic Variables
Non-Atomic Variables
Line 0
Line 1
Line 2
Line 3
Line 5
Random mapping  false sharing
An episode can only reserve and issue load/store operations to non-atomic variables associated with the atomic variable it acquires
Notes: Each atomic variable is associated with a range of normal variables

## Slide 72: GPU slicc protocol tester
Track per-variable last writers
  Who? (i.e., Lane ID, Wavefront ID, CU ID, and Episode ID)
  What value was written?
  When did the store operation happen?
For a Load (X), check if return value of X is equal to value written by the last writer to X. The last writer of X could be
  Either the last ST  X in the same episode, or
  The last ST  X in a previous episode
For an Atomic (A)
  Use atomic_inc: increment A by 1 atomically
  Track how many atomics have been issued so far. Let’s say N.
  Return value must be unique in the range [0..N-1] inclusively
Validation
Notes: Who? What CU, what Lane, what Episode?

## Slide 73: GPU slicc protocol tester
Forward progress check
  Report all outstanding requests that have been pending for more than a certain threshold
  Report their target addresses, lane IDs, CU IDs, CPU IDs, and episode IDs
Inconsistency between a Reader and its last Writer (the most common failure!)
Unexpected atomic return
  Report all expected return values
  Report address, lane ID, CU ID, and episode ID
The report really helps trace protocol bugs down quickly and precisely!
Failure report
Notes:   Now you know something was wrong btw tick 8454382 and the current tick -> trace the bug

## Slide 74: GPU slicc protocol tester
Available configurations
  Cache size
  Address range - # of atomic and normal variables
  System size - # CUs and #CPUs
  Episode length - # of LDs and STs per episode
  Test length - # of episodes
Example testing scenarios
  Small cache size + Wide address range
    Working set is much larger than the cache size
    Likely to expose bugs related to cache replacement
  Large cache size + Small address range
    Likely to expose bugs related to cache coherence (e.g., values are not passed between private caches correctly)
  Long episode length
    Conflicting accesses in the same episode
Testing options and scenarios

## Slide 75: Outline
Topic | Presenter | Time
Background | Tony | 8:00 – 8:15
ROCm, GCN3 ISA, and GPU Arch | Tony | 8:15 – 9:15
HSA Implementation in gem5 | Sooraj | 9:15 – 10:00
Break |  | 10:00 – 10:30
Ruby and GPU Protocol Tester | Tuan | 10:30 – 11:15
Demo and Workloads | Matt | 11:15 – 11:50
Summary and Questions | All | 11:50 – 12:00

## Slide 76: HIPIFY’ING CUDA BENCHMARKS
HIP code is easy to write if you have experience with CUDA
Hipify-perl can automatically convert most CUDA code to HIP code
  Works well for simple applications (e.g., no library calls)
  Perl regular expression replacement script
  Very simple, easy to use (as long as no library calls), fast
Useful HIP Information:
  Basic Intro to HIP
  Basic HIP Tutorial
  HIP Porting Guide
  Platform-Aware Coding

## Slide 77: Outline
Topic | Presenter | Time
Background | Tony | 8:00 – 8:15
ROCm, GCN3 ISA, and GPU Arch | Tony | 8:15 – 9:15
HSA Implementation in gem5 | Sooraj | 9:15 – 10:00
Break |  | 10:00 – 10:30
Ruby and GPU Protocol Tester | Tuan | 10:30 – 11:15
Demo and Workloads | Matt | 11:15 – 11:50
Summary and Questions | All | 11:50 – 12:00

## Slide 78: Comparison to other GPU Simulators
GPGPU-Sim
  Primarily focused on running Nvidia PTX instructions and CUDA applications
  Functional CPU model, oriented to model discrete GPU systems
  Wisconsin’s gem5-gpu added gem5 timing CPU models
    And a Ruby memory system protocol
  Differences from gem5-GPU:
    GCN3 instructions and ROCm software stack
    Unified under the gem5 source control repo
Multi2Sim
  Supports multiple ISAs including AMD Southern Island’s Machine ISA
  Limited instruction support
  No transient states in coherence protocol
This is very different than the gem5 NoMALI emulated GPU device

## Slide 79: Obvious improvements
Other GPU ISAs
Complete IOMMU model
Add graphics functionality
  Currently compute only
Better register model
  Simple register pool manager: one WG per CU
Remove backing store for memory data
  When running applications, the data from the caches is not used

## Slide 80: Summary
Covered a very high-level overview of:
  Introduction to the gem5 APU simulator
  Mapping between APU system and gem5 APU simulator
Topics discussed
  HSA and GCN Background
  Compilation and Simulation Flow
  GPU Core modules
  GPU memory system model in Ruby
  GPU protocol tester
  Comparisons/Improvements
Much more detail in the gem5 source code
Please contribute back to this community tool!

## Slide 81: Thank you
Alex Dutu
Ali Jafri
Arka Basu
Ayse Yilmazer
Binh Pham
Blake Hechtman
Brad Beckmann
Brandon Potter
Can Hankendi
David Hashe
Many Contributors over the past 8+ years
John Alsop
John Kalamatianos
Kishore Punniyamurthy
Kunal Korgaonkar
Lisa Hsu
Manish Arora
Marc Orr
Mario Mendez-Lojo
Mark Leather
Mark Wilkening
Martin Brown
David Roberts
Derek Hower
Dmitri Yudanov
Eric Van Tassell
Gagan Sachdev
James Wang
Jason Power
Joel Hestness
Jieming Yin
Joe Gross
Matt Poremba
Matt Sinclair
Michael LeBeane
Mike Chu
Myrto Papadopoulou
Monir Mozumder
Nagesh Lakshminarayana
Nilay Vaish
Onur Kayiran
Srikant Bharadwaj
Shrikanth Ganapathy
Si Li
Sooraj Puthoor
Steve Reinhardt
Tanmay Gangwani
Tim Rogers
Tony Gutierrez
Tsung Tai Yeh
Tushar Krishna
Xianwei Zhang
Yatin Manerkar
Yasuko Eckert

## Slide 82: Disclaimer & Attribution
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
ATTRIBUTION
© 2018 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo, and combinations thereof are trademarks of Advanced Micro Devices, Inc. Other product names used in this publication are for identification purposes only and may be trademarks of their respective companies. OpenCL is a trademark of Apple Inc. used by permission of Khronos.