## Slide 1: GPU Computing Architecture
HiPEAC Summer School, July 2015
Tor M. Aamodt
aamodt@ece.ubc.ca
University of British Columbia
NVIDIA Tegra X1 die photo
/

## Slide 2: GPU Instruction Set Architecture (ISA)
NVIDIA defines a virtual ISA, called “PTX” (Parallel Thread eXecution)
More recently, Heterogeneous System Architecture (HSA) Foundation (AMD, ARM, Imagination, Mediatek, Samsung, Qualcomm, TI) defined the HSAIL virtual ISA.
PTX is Reduced Instruction Set Architecture (e.g., load/store architecture)
Virtual: infinite set of registers (much like a compiler intermediate representation)
PTX translated to hardware ISA by backend compiler (“ptxas”). Either at compile time (nvcc) or at runtime (GPU driver).

## Slide 3: Some Example PTX Syntax
Registers declared with a type:
.reg .pred p, q, r;
.reg .u16 r1, r2;
.reg .f64 f1, f2;
ALU operations
add.u32 x, y, z; // x = y + z
mad.lo.s32 d, a, b, c; // d = a*b + c
Memory operations:
ld.global.f32 f, [a];
ld.shared.u32 g, [b];
st.local.f64 [c], h
Compare and branch operations:
setp.eq.f32 p, y, 0; // is y equal to zero?
@p bra L1 // branch to L1 if y equal to zero

## Slide 4: Generic GPGPU Architecture

## Slide 5: Extra resources
GPGPU-Sim 3.x Manualhttp://gpgpu-sim.org/manual/index.php/GPGPU-Sim_3.x_Manual

## Slide 6: GPU Microarchitecture Overview
Single-Instruction, Multiple-Threads
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR5
Memory
Partition
GDDR5
Memory
Partition
GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 7: GPU Microarchitecture
Companies tight lipped about details of GPU microarchitecture.
Several reasons:
  Competitive advantage
  Fear of being sued by “non-practicing entities”
  The people that know the details too busy building the next chip
Model described next, embodied in GPGPU-Sim, developed from: white papers, programming manuals, IEEE Micro articles, patents.

## Slide 8
GPGPU-Sim v3.x w/ SASS
Correlation
~0.976
12
Chart: HW - GPGPU-Sim Comparison

## Slide 9: GPU Microarchitecture Overview
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 10: Inside a SIMT Core
SIMT front end / SIMD backend
Fine-grained multithreading
  Interleave warp execution to hide latency
  Register values of all threads stays in core
SIMT
Front End
SIMD Datapath
Fetch
Decode
Schedule
Branch
Memory Subsystem
Icnt.
Network
SMem
L1 D$
Tex $
Const$
Reg
File

## Slide 11: Inside an “NVIDIA-style” SIMT Core
SIMT Front End
SIMD Datapath
ALU
ALU
ALU
I-Cache
Decode
I-Buffer
Score
Board
Issue
Operand
Collector
MEM
ALU
Fetch
SIMT-Stack
Done (WID)
Valid[1:N]
Branch Target PC
Pred.
Active
Mask
Three decoupled warp schedulers
Scoreboard
Large register file
Multiple SIMD functional units
Scheduler 1
Scheduler 2
Scheduler 3

## Slide 12: Fetch + Decode
Arbitrate the I-cache among warps
  Cache miss handled by fetching again later
Fetched instruction is decoded and then stored in the I-Buffer
  1 or more entries / warp
  Only warp with vacant entries are considered in fetch
Inst. W1
r
Inst. W2
Inst. W3
v
r
v
r
v
To
Fetch
Issue
Decode
Score-
Board
Issue
ARB
PC
1
PC
2
PC
3
A
R
B
Selection
T
o
I
-
C
a
c
h
e
Valid[1:N]
I-Cache
Decode
I-Buffer
Fetch
Valid[1:N]

## Slide 13: Instruction Issue
Select a warp and issue an instruction from its I-Buffer for execution
  Scheduling: Greedy-Then-Oldest (GTO)
  GT200/later Fermi/Kepler: Allow dual issue (superscalar)
  Fermi: Odd/Even scheduler
  To avoid stalling pipeline might
  keep instruction in I-buffer until
  know it can complete (replay)

## Slide 14: Review: In-order Scoreboard
Scoreboard: a bit-array, 1-bit for each register
  If the bit is not set: the register has valid data
  If the bit is set: the register has stale data
    i.e., some outstanding instruction is going to change it
Issue in-order: RD  Fn (RS, RT)
  If SB[RS] or SB[RT] is set  RAW, stall
  If SB[RD] is set  WAW, stall
  Else, dispatch to FU (Fn) and set SB[RD]
Complete out-of-order
  Update GPR[RD], clear SB[RD]
Regs[R1]
Regs[R2]
Regs[R3]
Regs[R31]
1
0
0
0
Register File
Scoreboard
[Gabriel Loh]
+
Notes: H&P-style notation

## Slide 15: Example
- | - | - | -
- | - | - | -
Warp 0
Warp 1
ld r7, [r0]
mul r6, r2, r5
add r8, r6, r7
Index 0
Index 1
Scoreboard
Index 2
Warp 0
Warp 1
Instruction Buffer
i0 i1 i2 i3
Index 3
r7 | - | - | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
ld r7, [r0] | 0 | 0 | 0 | 0
mul r6, r2, r5 | 0 | 0 | 0 | 0
r7 | r6 | - | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
mul r6, r2, r5 | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 1 | 0 | 0
ld r7, [r0] | 0 | 0 | 0 | 0
mul r6, r2, r5 | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 1 | 0 | 0
r7 | r6 | r8 | -
- | - | - | -
r7 | r6 | r8 | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 0 | 0 | 0
r7 | - | r8 | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 0 | 0 | 0
r7 | - | r8 | -
- | - | - | -
add r8, r6, r7 | 0 | 0 | 0 | 0
- | - | r8 | -
- | - | - | -
Code
+

## Slide 16: SIMT Using a Hardware Stack
-
G
1111
TOS
B
C
D
E
F
A
G
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B/1111
C/1001
D/0110
E/1111
A/1111
G/1111
-
A
1111
TOS
E
D
0110
E
C
1001
TOS
-
E
1111
E
D
0110
TOS
-
E
1111
A
D
G
A
Time
C
B
E
-
B
1111
TOS
-
E
1111
TOS
Reconv. PC
Next PC
Active Mask
Stack
E
D
0110
E
E
1001
TOS
-
E
1111
Stack approach invented at Lucasfilm, Ltd in early 1980’s
SIMT = SIMD Execution of Scalar Threads
Version here from [Fung et al., MICRO 2007]

## Slide 17: Register File
32 warps, 32 threads per warp, 16 x 32-bit registers per thread = 64KB register file.
Need “4 ports” (e.g., FMA) greatly increase area.
Alternative: banked single ported register file. How to avoid bank conflicts?

## Slide 18: Banked Register File
Strawman microarchitecture:
Register layout:

## Slide 19: Register Bank Conflicts
warp 0, instruction 2 has two source operands in bank 1: takes two cycles to read.
Also, warp 1 instruction 2 is same and is also stalled.
Can use warp ID as part of register layout to help.

## Slide 20: Operand Collector
Term “Operand Collector” appears in figure in NVIDIA Fermi Whitepaper
Operand Collector Architecture (US Patent: 7834881)
  Interleave operand fetch from different threads to achieve full utilization
Bank 0
Bank 1
Bank 2
Bank 3
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
…
…
…
…
add.s32 R3, R1, R2;
No Conflict
mul.s32 R3, R0, R4;
Conflict at bank 0

## Slide 21: Operand Collector (1)
Issue instruction to collector unit.
Collector unit similar to reservation station in tomasulo’s algorithm.
Stores source register identifiers.
Arbiter selects operand accesses that do not conflict on a given cycle.
Arbiter needs to also consider writeback (or need read+write port)

## Slide 22: Operand Collector (2)
Combining swizzling and access scheduling can give up to ~ 2x improvement in throughput

## Slide 23: GPU Memory Address Spaces
GPU has three address spaces to support increasing visibility of data between threads: local, shared, global
In addition two more (read-only) address spaces: Constant and texture.

## Slide 24: Local (Private) Address Space
Each thread has own “local memory” (CUDA) “private memory” (OpenCL).
0x42
Note: Location at address 100 for thread 0 is different from location at address 100 for thread 1.
Contains local variables private to a thread.

## Slide 25: Global Address Spaces
thread block X
thread block Y
Each thread in the different thread blocks (even from different kernels) can access a region called “global memory” (CUDA/OpenCL).
Commonly in GPGPU workloads threads write their own portion of global memory. Avoids need for synchronization—slow; also unpredictable thread block scheduling.
0x42

## Slide 26: Shared (Local) Address Space
Each thread in the same thread block (work group) can access a memory region called “shared memory” (CUDA) “local memory” (OpenCL).
Shared memory address space is limited in size (16 to 48 KB).
Used as a software managed “cache” to avoid off-chip memory accesses.
Synchronize threads in a thread block using __syncthreads();
thread block
0x42

## Slide 27: Review: Bank Conflicts
To increase bandwidth common to organize memory into multiple banks.
Independent accesses to different banks can proceed in parallel
Bank 0
Bank 1
0 | 
2 | 
4 | 
6 | 
1 | 
3 | 
5 | 
7 | 
Example 1: Read 0, Read 1
(can proceed in parallel)
Example 2: Read 0, Read 3
(can proceed in parallel)
Bank 0
Bank 1
0 | 
2 | 
4 | 
6 | 
1 | 
3 | 
5 | 
7 | 
Example 3: Read 0, Read 2
(bank conflict)
Bank 0
Bank 1
0 | 
2 | 
4 | 
6 | 
1 | 
3 | 
5 | 
7 | 

## Slide 28: Shared Memory Bank Conflicts
__shared__ int A[BSIZE];
…
A[threadIdx.x] = … // no conflicts
0 | 
32 | 
64 | 
96 | 
1 | 
33 | 
65 | 
97 | 
31 | 
63 | 
95 | 
127 | 
2 | 
34 | 
66 | 
98 | 

## Slide 29: Shared Memory Bank Conflicts
__shared__ int A[BSIZE];
…
A[2*threadIdx.x] = // 2-way conflict
0 | 
32 | 
64 | 
96 | 
1 | 
33 | 
65 | 
97 | 
31 | 
63 | 
95 | 
127 | 
2 | 
34 | 
66 | 
98 |